## Slide 1: Vastestoffysica VI
Saskia Blom
(s.blom@fontys.nl)
http://www.phys.ufl.edu/fermisurface/
Notes: https://classes.soe.ucsc.edu/ee145/Spring02/EE145hmwk4Sol.pdf

## Slide 2
Ex
Ez
bol met straal EF
Ey
straal EF
toestanden met
E < EF
Ey
Ez
Ex
Fermi-oppervlak
http://www.ugrad.physics.mcgill.ca/wiki/index.php/PHYS-558
http://www.learner.org/courses/physics/unit/text.html?unit=8&secNum=2
http://www.phys.ufl.edu/fermisurface/
Fermi-oppervlak
voor koper (fcc)
http://www.phys.ufl.edu/fermisurface/jpg/K.jpg
Fermi-oppervlak
voor kalium (bcc)
http://www.phys.ufl.edu/fermisurface/jpg/Cu.jpg
Notes: Als # hokjes geteld wordt als functie van E  g(E). Als # hokjes geteld wordt als functie van p  g(p): dan is faseruimte een hele bol (ipv 1/8), hiervoor corrigeert het verschil tussen g(p) en g(E)
The ground state of the electrons moving in a uniform background of positive charge would then be a simple sphere in momentum space bounded by its Fermi surface, a concept derived from the statistical work of Enrico Fermi and P.A.M. Dirac that defines the energies of electrons in a metal. When the uniform positive charge is replaced by the actual periodic array of the ions in a metallic lattice, the simple sphere becomes a more complex geometric structure that reflects the nature of the underlying ionic periodic structure, an example of which is shown in Figure 6.
http://www.learner.org/courses/physics/unit/text.html?unit=8&secNum=2
http://www.phys.ufl.edu/fermisurface/

## Slide 3
Fermi-oppervlak: verbindt hoogste energietoestanden
http://hyperphysics.phy-astr.gsu.edu/hbase/solids/fermi2.html
elektronen onderscheiden zich via spin, positie, hoogte vd kinetische energie,
en de richting van de impuls horend bij deze kinetische energie
Blokje koper van 1cm3: zeer veel valentie-elektronen
Heisenberg: op dezelfde positie kunnen maar twee e- met dezelfde impuls zijn
Notes: Als # hokjes geteld wordt als functie van E  g(E). Als # hokjes geteld wordt als functie van p  g(p): dan is faseruimte een hele bol (ipv 1/8), hiervoor corrigeert het verschil tussen g(p) en g(E). When you apply a voltage to a copper wire, you establish an electric field in the wire which can do work on the electrons to give them energy. But the example of copper wire conduction shows that the mean free path of electrons in a copper wire at room temperature is in the neighborhood of 40 nm. So the energy given to an electron by the electric field by 100 volts applied to a 1 meter copper wire would be on the order of W=eEd = 100 volts x 40 nm = 0.000004 eV. Such an amount of energy cannot be absorbed by most of the electrons because there is no available energy level that close to them in energy.
http://hyperphysics.phy-astr.gsu.edu/hbase/electric/ohmmic.html#c2

## Slide 4
Ten opzichte waarvan is EF gedefinieerd?
ten opzichte van:
de situatie waar geen krachten werken
de maximale energie van de e- bij T=0K
de bodem van de potentiaalput
de uittree-arbeid (work function)
Quiz Fermi-energie
Notes: http://www.tf.uni-kiel.de/matwis/amat/semi_en/kap_2/backbone/r2_2_4.html

## Slide 5
EF d
Uittreearbeid (werkfunctie) en EF
0V
EF
laagste energietoestand van valentie e- in metaalrooster
laagste energietoestand van gebonden e- in atoom
uittreearbeid F
(work function):
minimale arbeid nodig om
één e- uit metaalrooster
vrij te maken
Fermi-energie EF:
bepaalt samen met F
diepte van de potentiaalput V0
(F voor sterkst gebonden e-)
eV0 = EF + e F
Notes: Photoelectric diode in forward bias configuration, used for measuring the work function We of the illuminated emitter. http://en.wikipedia.org/wiki/Work_function
Als materiaal voor de kathode gebruikt men vaak wolfraam, omdat dat metaal goed bestand is tegen hoge temperaturen. Omdat wolfraam van zichzelf een hoge uittreepotentiaal heeft (~4,5 eV), bedekt men het met een laagje BaO en SrO om deze potentiaal te verlagen tot ~1 eV. De werktemperatuur van dergelijke oxidekathoden ligt rond de 1000 °C. De relatie tussen de temperatuur van de kathode, uittreepotentiaal van het kathodemateriaal en de uit de kathode tredende stroomdichtheid wordt gegeven door de formule van Richardson.

## Slide 6
  Bandenstructuur: halfgeleiders
  Dotering
  pn-overgang (Diode)
Inhoud college vandaag

## Slide 7
Effect van temperatuur op verdeling valentie-e-
http://cnx.org/content/m13458/latest/
  geleider
  isolator
  Ferminiveau isolator: EF=½ (EC+EV)
  EV: energie hoogste gevulde energieniveau bij T  0 K
  EC: energie dat 1e toegevoegd e- vervolgens moet hebben
T > 0 K
T0 K
Notes:   Ferminiveau isolator: EF=½ (EC+EV) want kans op e- in geleidingsband moet even groot zijn als kans op gat in valentieband (impliceert elkaar)
Vastestoffysica: kristallen (simpelste stoffen om te bestuderen) hoe gedragen elektronen in kristallen zich? Hieruit geleidingsgedrag en warmtecapaciteit te berekenen.

## Slide 8
Fermi-Dirac statistiek: kans dat deeltje energie E heeft
http://en.wikipedia.org/wiki/Fermi–Dirac_statistics
http://en.wikipedia.org/wiki/File:Fermi.gif
grote T
kleine T
m: Ferminiveau

## Slide 9
Effect van temperatuur op verdeling valentie-e-
http://cnx.org/content/m13458/latest/
  geleider
  isolator
T0 K
T > 0 K
kans om bij deze E
een e- aan te treffen
Notes:   Ferminiveau isolator: EF=½ (EC+EV) want kans op e- in geleidingsband moet even groot zijn als kans op gat in valentieband (impliceert elkaar)
3 getekende e- is indicatie voor kans om bij overeenkomende E een e- aan te treffen
Vastestoffysica: kristallen (simpelste stoffen om te bestuderen) hoe gedragen elektronen in kristallen zich? Hieruit geleidingsgedrag en warmtecapaciteit te berekenen.

## Slide 10
Effect van temperatuur op verdeling valentie-e-
http://cnx.org/content/m13458/latest/
  geleider
  isolator
T0 K
T > 0 K
  Ferminiveau isolator: EF=½ (EC+EV)
  EV: energie hoogste gevulde energieniveau bij T  0 K
  EC: energie dat 1e toegevoegd e- vervolgens moet hebben
  band gap EG = EC- EV
  conduction band:
  e- mobiel  geleiding
  valence band:
  e- immobiel
Notes:   Ferminiveau isolator: EF=½ (EC+EV) want kans op e- in geleidingsband moet even groot zijn als kans op gat in valentieband (impliceert elkaar)
Vastestoffysica: kristallen (simpelste stoffen om te bestuderen) hoe gedragen elektronen in kristallen zich? Hieruit geleidingsgedrag en warmtecapaciteit te berekenen.

## Slide 11
Bij kamertemperatuur geldt: kT ~ 0,025 eV
Schat ordegrootte van # e- in de geleidingsband, in een rooster met 10 21 atomen
Schat # e- in geleidingsband
Example 40-13: Free electrons in semiconductors and insulators
a) Si: Eg = 1,1 eV
 E – EF = ?
b) Eg = 5 eV
 E – EF = ?
f(E) ≈ e –22 ≈ 10-10
1011 mobiele e-
 E – EF = 0,55 eV
 E – EF = 2,5 eV
f(E) ≈ e –100 ≈ 10-44
in rooster: 10-23: geen mobiele e-
c) Vergelijk met geleider
in metaalrooster: 10 21 vrije e-
isolator
Notes: Diamant 5,5 eV
Solution: For semiconductors and insulators the Fermi energy can be taken to be halfway through the energy gap. At room temperature, kT = 0.026 eV.
a. Substituting gives f(E) ≈ 10-9.
b. Substituting gives f(E) ≈ 10-42.
In a conductor, there is one free electron per atom, or 1021. In a semiconductor, there will be 1012 free electrons, and in an insulator there will be none.
Kamertemperatuur: 1/40 = 0,025 eV

## Slide 12
  Bandentheorie:
    metaal: overlap van valentieband en geleidingsband.
    isolator en halfgeleider: valentieband geheel gevuld, iets hogere energie is verboden. Eerstvolgende toegestane energietoestand is in de conductieband.
    bandgap is bij isolator veel groter dan bij halfgeleider.
Metaal / isolator / halfgeleider
valentieband: vrije e-
in overvolle energieniveaus
 Ekin van e- kan niet omhoog
conductieband: vrije e-
kunnen versneld worden 
er kan een stroom lopen
geen energieniveaus
beschikbaar
Notes: Vastestoffysica: kristallen (simpelste stoffen om te bestuderen) hoe gedragen elektronen in kristallen zich? Hieruit geleidingsgedrag en warmtecapaciteit te berekenen.

## Slide 13: §40.8 Elektronen- en gatengeleiding in Si
http://hyperphysics.phy-astr.gsu.edu/hbase/solids/sili2.html
Notes: Figure 40-34. Two-dimensional representation of a silicon crystal. (a) Four (outer) electrons surround each silicon atom. (b) Silicon crystal doped with a small percentage of arsenic atoms: the extra electron doesn’t fit into the crystal lattice and so is free to move about. This is an n-type semiconductor.

## Slide 14
Gatengeleiding
    elektronen schuiven op (collectief, niet individueel)
    vacatures  gaten: opvatten als positief ‘deeltje’
Notes: Vastestoffysica: kristallen (simpelste stoffen om te bestuderen) hoe gedragen elektronen in kristallen zich? Hieruit geleidingsgedrag en warmtecapaciteit te berekenen.

## Slide 15
valentieband: e- -gaten
(~ luchtmoleculen)
conductieband: vrije e-
(~ watermoleculen)
geen energieniveaus
beschikbaar
Halfgeleider
    geleidingsband (bijna leeg)
    verboden energiekloof
    valentieband (overvol)
Notes: Vastestoffysica: kristallen (simpelste stoffen om te bestuderen) hoe gedragen elektronen in kristallen zich? Hieruit geleidingsgedrag en warmtecapaciteit te berekenen.

## Slide 16
§40.8 Halfgeleiders en doteren
Fosfor-dotering (15P) in silicium (14Si): n-type halfgeleider
(overschot negatieve ladingsdragers)
Si: 3s2 3p2
P: 3s2 3p3
Notes: Figure 40-35. A p-type semiconductor, gallium-doped silicon. (a) Gallium has only three outer electrons, so there is an empty spot, or hole in the structure. (b) Electrons from silicon atoms can jump into the hole and fill it. As a result, the hole moves to a new location (to the right in this Figure), to where the electron used to be.

## Slide 17
Arseen-dotering in silicium: n-type halfgeleider
(overschot negatieve ladingsdragers)
§40.8 Halfgeleiders en doteren
Si: 3s2 3p2
As: 4s2 4p3
Notes: Figure 40-34. Two-dimensional representation of a silicon crystal. (a) Four (outer) electrons surround each silicon atom. (b) Silicon crystal doped with a small percentage of arsenic atoms: the extra electron doesn’t fit into the crystal lattice and so is free to move about. This is an n-type semiconductor.

## Slide 18
Periodiek systeem
http://www.ptable.com/?lang=nl#Orbital

## Slide 19
Gallium-dotering in silicium: p-type halfgeleider
(overschot positieve ladingsdragers: gaten)
§40.8 Halfgeleiders en doteren
Notes: Figure 40-35. A p-type semiconductor, gallium-doped silicon. (a) Gallium has only three outer electrons, so there is an empty spot, or hole in the structure. (b) Electrons from silicon atoms can jump into the hole and fill it. As a result, the hole moves to a new location (to the right in this Figure), to where the electron used to be.

## Slide 20
De onzuiverheid levert extra energietoestanden in de halfgeleider.
§40.8 Halfgeleiders en doteren
Notes: Figure 40-36. Impurity energy levels in doped semiconductors.

## Slide 21
  Doteren van halfgeleider: lokaal verontreinigen met
    atoom met lagere waardigheid: p-type (gaten geleiden)
    (Groep-III element; acceptor)
    atoom met hogere waardigheid: n-type (e- geleiden)
    (Groep-V element; elektrondonor)
  Doteringstechnieken:
    Diffusie
    Implantatie van ionen
http://www.tf.uni-kiel.de/matwis/amat/semi_en/kap_2/backbone/r2_3_5.html
boor, aluminium, gallium
fosfor; arseen
http://www.superstrate.net/pv/physics/doping.html
40.8 Dotering (Doping)
Notes: Halfgeleider uit groep IV (Silicium, Germanium
Groep III: Boor, Gallium, Indium, Aluminium
Groep V: Fosfor; Arseen; Stikstof, Antimoon, Bismuth
http://www.hk-phy.org/energy/alternate/solar_phy03_e.html
http://www.see.murdoch.edu.au/resources/info/Tech/pv/
http://www.tf.uni-kiel.de/matwis/amat/semi_en/kap_2/backbone/r2_3_5.html
http://peterdoggart.com/wp-content/uploads/2012/10/Diode-Characteristics.pdf
When on the order of one dopant atom is added per 100 million atoms, the doping is said to be low or light. When many more dopant atoms are added, on the order of one per ten thousand atoms, the doping is referred to as heavy or high. This is often shown as n+ for n-type doping or p+ for p-type doping. (sensitors heavy; NTC and PTC light)

## Slide 22
Ferminiveau bij T  0K
halverwege boven
het donorniveau
40.8 Dotering (Doping)
Gecontroleerd vervuilen van Si:
Notes: Figure 40-36. Impurity energy levels in doped semiconductors.
http://hyperphysics.phy-astr.gsu.edu/hbase/solids/dsem.html

## Slide 23
gedoteerde halfgeleider geleidt beter dan
zuivere halfgeleider
bij T  0K
40.8 Dotering (Doping)
Gecontroleerd vervuilen van Si:
niet op tentamen
Notes: Figure 40-36. Impurity energy levels in doped semiconductors.
http://hyperphysics.phy-astr.gsu.edu/hbase/solids/dsem.html

## Slide 24
(goede) benadering:
T > 0 K 
alle elektronen van donor in geleidingsband &
elk acceptor-atoom veroorzaakt gat
dotering 1 op 106 atomen:
Stel: 1021 atomen
verhouding (nd + ni) / ni
bij lagere T: (1015 + 1012) /(1012)
bij hoge T: (1015 + 1014) /(1014)  1
dus Ferminiveau richting midden bandgap
als T  : Ferminiveau richting midden bandgap
40.8 Dotering (Doping)
Notes: Figure 40-36. Impurity energy levels in doped semiconductors.
http://hyperphysics.phy-astr.gsu.edu/hbase/solids/dsem.html

## Slide 25
bij lagere T: (1015 + 1012) /(1012) 
dotering heeft groot effect
bij hoge T: (1015 + 1014) /(1014)  1
dus Ferminiveau richting midden bandgap
Temperatuurafhankelijkheid Ferminiveaus
Stel: 1021 atomen,
dotering 1 op 106 atomen
Verhouding (e- in C) : (gaten in V):
(nd + ni) / ni
Notes: Figure 40-36. Impurity energy levels in doped semiconductors.
http://hyperphysics.phy-astr.gsu.edu/hbase/solids/dsem.html

## Slide 26
dotering 1 op 106 atomen:
Stel: 1021 atomen
verhouding (nd + ni) / ni
bij lagere T: (1015 + 1012) /(1012)
bij hoge T: (1015 + 1014) /(1014)  1
dus Ferminiveau richting midden bandgap
weinig mobiele e-
veel gaten
veel mobiele e-
weinig gaten
40.8 Dotering (Doping)
Gecontroleerd vervuilen van Si:
wel op tentamen
Notes: Figure 40-36. Impurity energy levels in doped semiconductors.
http://hyperphysics.phy-astr.gsu.edu/hbase/solids/dsem.html

## Slide 27
  Bandentheorie:
    Door dotering met elektron-acceptor komt p-type halfgeleider hoger te liggen
    Door dotering met elektron-donor komt n-type halfgeleider lager te liggen
Metaal / halfgeleider / isolator
Notes: Vastestoffysica: kristallen (simpelste stoffen om te bestuderen) hoe gedragen elektronen in kristallen zich? Hieruit geleidingsgedrag en warmtecapaciteit te berekenen.

## Slide 28
Hoe ontstaan er gaten (electron holes) in een n-type materiaal?
De negatieve lading in het n-type materiaal trekt gaten aan.
Een e- van de elektrondonor springt tgv thermische energie naar de geleidingsband.
Een e- uit de valentieband springt tgv thermische energie naar de geleidingsband.
Quiz
neutraal!
er blijft géén gat achter;
het 5e e- (groep-V element) komt in valentieband
http://www.allaboutcircuits.com/vol_3/chpt_2/5.html
Notes: http://astarmathsandphysics.com/a-level-physics-notes/electronics/a-level-physics-notes-electronics-n-and-p-type-semiconductors.html

## Slide 29
  Combinatie van dotering van halfgeleider met e--acceptor (p-type) en halfgeleider met e--donor (n-type)
p-n overgang (p-n junction)
Notes: take out one atom and replace it with an atom from an adjacent group in the periodic system. If the replacing atom is from a group to the right, it will have an extra electron which is not needed in the original bonding configuration. The most prominent example is phosphorus in silicon. In the tetrahedral bonding configuration of silicon four electrons are needed for the bonding to the four neighbours. Obviously, the fifth electron of phosphorus is not needed for the bonding. We may assume that the single, weakly bound extra electron feels a potential similar to the electron in the hydrogen atom, but extending downwards from the conduction band.
Doping with donors raises the Fermi level from the midgap position closer to the conduction band.
intrinsic carrier density is independent of doping, since EC - EV (the band gap) does not change with doping.. Intrinsic carrier concentration varies between materials and is dependent on temperature. Silicon's ni, for example, is roughly 1.08×1010 cm−3 at 300 kelvin (room temperature).[4]
In crystalline intrinsic silicon, there are approximately 5×1022 atoms/cm³. Doping concentration for silicon semiconductors may range anywhere from 1013 cm−3 to 1018 cm−3. Doping concentration above about 1018 cm−3 is considered degenerate at room temperature. Degenerately doped silicon contains a proportion of impurity to silicon on the order of parts per thousand. This proportion may be reduced to parts per billion in very lightly doped silicon

## Slide 30
  Combinatie van dotering van halfgeleider met e--acceptor (p-type) en halfgeleider met e--donor (n-type)
p-n overgang (p-n junction)
recombinatie van gaten en e-: dit creëert ruimtelading
Notes: take out one atom and replace it with an atom from an adjacent group in the periodic system. If the replacing atom is from a group to the right, it will have an extra electron which is not needed in the original bonding configuration. The most prominent example is phosphorus in silicon. In the tetrahedral bonding configuration of silicon four electrons are needed for the bonding to the four neighbours. Obviously, the fifth electron of phosphorus is not needed for the bonding. We may assume that the single, weakly bound extra electron feels a potential similar to the electron in the hydrogen atom, but extending downwards from the conduction band.
Doping with donors raises the Fermi level from the midgap position closer to the conduction band.
intrinsic carrier density is independent of doping, since EC - EV (the band gap) does not change with doping.. Intrinsic carrier concentration varies between materials and is dependent on temperature. Silicon's ni, for example, is roughly 1.08×1010 cm−3 at 300 kelvin (room temperature).[4]
In crystalline intrinsic silicon, there are approximately 5×1022 atoms/cm³. Doping concentration for silicon semiconductors may range anywhere from 1013 cm−3 to 1018 cm−3. Doping concentration above about 1018 cm−3 is considered degenerate at room temperature. Degenerately doped silicon contains a proportion of impurity to silicon on the order of parts per thousand. This proportion may be reduced to parts per billion in very lightly doped silicon

## Slide 31
  Combinatie van dotering van halfgeleider met e--acceptor (p-type) en halfgeleider met e--donor (n-type)
p-n overgang (p-n junction)
Hoe onstaat er licht in een diode ?
recombinatie van gaten en e-: dit creëert ruimtelading
E
-|Emax|
Notes: take out one atom and replace it with an atom from an adjacent group in the periodic system. If the replacing atom is from a group to the right, it will have an extra electron which is not needed in the original bonding configuration. The most prominent example is phosphorus in silicon. In the tetrahedral bonding configuration of silicon four electrons are needed for the bonding to the four neighbours. Obviously, the fifth electron of phosphorus is not needed for the bonding. We may assume that the single, weakly bound extra electron feels a potential similar to the electron in the hydrogen atom, but extending downwards from the conduction band.
Doping with donors raises the Fermi level from the midgap position closer to the conduction band.
intrinsic carrier density is independent of doping, since EC - EV (the band gap) does not change with doping.. Intrinsic carrier concentration varies between materials and is dependent on temperature. Silicon's ni, for example, is roughly 1.08×1010 cm−3 at 300 kelvin (room temperature).[4]
In crystalline intrinsic silicon, there are approximately 5×1022 atoms/cm³. Doping concentration for silicon semiconductors may range anywhere from 1013 cm−3 to 1018 cm−3. Doping concentration above about 1018 cm−3 is considered degenerate at room temperature. Degenerately doped silicon contains a proportion of impurity to silicon on the order of parts per thousand. This proportion may be reduced to parts per billion in very lightly doped silicon

## Slide 32
(δίοδος=bergpas)
pn-overgang
er stelt zich een evenwicht in tussen
drift- en diffusiestromen
Notes: https://fisluisabraham.files.wordpress.com/2014/08/krane-k-modern-physics-3ed.pdf

## Slide 33
  Combinatie van dotering van halfgeleider met e--acceptor (p-type) en halfgeleider met e--donor (n-type)
p-n overgang (junction)
recombinatie gaten en e-
Wat gebeurt er als er spanning op wordt gezet?
Notes: take out one atom and replace it with an atom from an adjacent group in the periodic system. If the replacing atom is from a group to the right, it will have an extra electron which is not needed in the original bonding configuration. The most prominent example is phosphorus in silicon. In the tetrahedral bonding configuration of silicon four electrons are needed for the bonding to the four neighbours. Obviously, the fifth electron of phosphorus is not needed for the bonding. We may assume that the single, weakly bound extra electron feels a potential similar to the electron in the hydrogen atom, but extending downwards from the conduction band.
Doping with donors raises the Fermi level from the midgap position closer to the conduction band.
intrinsic carrier density is independent of doping, since EC - EV (the band gap) does not change with doping.. Intrinsic carrier concentration varies between materials and is dependent on temperature. Silicon's ni, for example, is roughly 1.08×1010 cm−3 at 300 kelvin (room temperature).[4]
In crystalline intrinsic silicon, there are approximately 5×1022 atoms/cm³. Doping concentration for silicon semiconductors may range anywhere from 1013 cm−3 to 1018 cm−3. Doping concentration above about 1018 cm−3 is considered degenerate at room temperature. Degenerately doped silicon contains a proportion of impurity to silicon on the order of parts per thousand. This proportion may be reduced to parts per billion in very lightly doped silicon

## Slide 34: 40.9 Semiconductor Diodes
(δίοδος=bergpas)
http://www.pveducation.org/pvcdrom/pn-junction/diode-equation
pn-overgang in doorlaatrichting
In een LED ontstaat licht via recombinatie e- en gat
depletielaag wordt kleiner
als V groot genoeg: geleiding
Notes: http://cnx.org/content/m1008/latest/
Figure 40-37. Schematic diagram showing how a semiconductor diode operates. Current flows when the voltage is connected in forward bias, as in (a), but not when connected in reverse bias, as in (b).
Study of band structure also led to the ability to create a population inversion in a III-V material for the lasing process to be possible for the laser diode. Peltier coolers, often used on CCDs and microprocessors, have been invented by studying phonon interactions of solids. http://www.pha.jhu.edu/~jeffwass/2ndYrSem/slide3.html

## Slide 35: 40.9 Semiconductor Diodes
(δίοδος=bergpas)
http://www.pveducation.org/pvcdrom/pn-junction/diode-equation
  pn-overgang in sperstand
na thermisch aanslaan e- in depletielaag
(creatie e- -gatpaar)
worden gat en e- uit elkaar gedreven
 lekstroom - donkerstroom
Notes: http://cnx.org/content/m1008/latest/
Figure 40-37. Schematic diagram showing how a semiconductor diode operates. Current flows when the voltage is connected in forward bias, as in (a), but not when connected in reverse bias, as in (b).
Study of band structure also led to the ability to create a population inversion in a III-V material for the lasing process to be possible for the laser diode. Peltier coolers, often used on CCDs and microprocessors, have been invented by studying phonon interactions of solids. http://www.pha.jhu.edu/~jeffwass/2ndYrSem/slide3.html

## Slide 36
http://www.pveducation.org/pvcdrom/pn-junction/diode-equation
pn-overgang
teken de ladingen
op de pn-overgang
Notes: http://cnx.org/content/m1008/latest/
Figure 40-37. Schematic diagram showing how a semiconductor diode operates. Current flows when the voltage is connected in forward bias, as in (a), but not when connected in reverse bias, as in (b).
Study of band structure also led to the ability to create a population inversion in a III-V material for the lasing process to be possible for the laser diode. Peltier coolers, often used on CCDs and microprocessors, have been invented by studying phonon interactions of solids. http://www.pha.jhu.edu/~jeffwass/2ndYrSem/slide3.html

## Slide 37
pn-overgang
teken het E-veld
http://www.pveducation.org/pvcdrom/pn-junction/diode-equation
+
-
-
+
Notes: http://cnx.org/content/m1008/latest/
Figure 40-37. Schematic diagram showing how a semiconductor diode operates. Current flows when the voltage is connected in forward bias, as in (a), but not when connected in reverse bias, as in (b).
Study of band structure also led to the ability to create a population inversion in a III-V material for the lasing process to be possible for the laser diode. Peltier coolers, often used on CCDs and microprocessors, have been invented by studying phonon interactions of solids. http://www.pha.jhu.edu/~jeffwass/2ndYrSem/slide3.html

## Slide 38
pn-overgang
http://www.pveducation.org/pvcdrom/pn-junction/diode-equation
E
-|Emax|
E-veld tegengesteld aan doorlaatrichting
Notes: http://cnx.org/content/m1008/latest/
Figure 40-37. Schematic diagram showing how a semiconductor diode operates. Current flows when the voltage is connected in forward bias, as in (a), but not when connected in reverse bias, as in (b).
Study of band structure also led to the ability to create a population inversion in a III-V material for the lasing process to be possible for the laser diode. Peltier coolers, often used on CCDs and microprocessors, have been invented by studying phonon interactions of solids. http://www.pha.jhu.edu/~jeffwass/2ndYrSem/slide3.html

## Slide 39
pn-overgang
teken energiediagram voor e-
http://www.pveducation.org/pvcdrom/pn-junction/diode-equation
Notes: http://cnx.org/content/m1008/latest/
Figure 40-37. Schematic diagram showing how a semiconductor diode operates. Current flows when the voltage is connected in forward bias, as in (a), but not when connected in reverse bias, as in (b).
Study of band structure also led to the ability to create a population inversion in a III-V material for the lasing process to be possible for the laser diode. Peltier coolers, often used on CCDs and microprocessors, have been invented by studying phonon interactions of solids. http://www.pha.jhu.edu/~jeffwass/2ndYrSem/slide3.html

## Slide 40
(δίοδος=bergpas)
pn-overgang
http://www.pveducation.org/pvcdrom/pn-junction/diode-equation
Notes: http://cnx.org/content/m1008/latest/
Figure 40-37. Schematic diagram showing how a semiconductor diode operates. Current flows when the voltage is connected in forward bias, as in (a), but not when connected in reverse bias, as in (b).
Study of band structure also led to the ability to create a population inversion in a III-V material for the lasing process to be possible for the laser diode. Peltier coolers, often used on CCDs and microprocessors, have been invented by studying phonon interactions of solids. http://www.pha.jhu.edu/~jeffwass/2ndYrSem/slide3.html

## Slide 41
pn-overgang
http://www.intechopen.com/books/photodiodes-world-activities-in-2011/cmos-photodetectors
bandgap
depletielaag
(uitputtingszone)
potentiaal e-
configuratie
ruimte-
lading
meerderheids-
ladingsdragers
https://www.pveducation.org/pvcdrom/solving-for-depletion-region
Nd
Na
mobiele ladingsdragers versus ruimtelading
Notes: Diffusion of carriers at the p-n junction, (b) the resulting electron and hole density distribution, where Na and Nd are the acceptors and donors densities, (c) the resulting charge density distribution, (d) the resulting electric field, and (e) the band diagram of a p-n junction showing the alignment of the Fermi level, Ef, and shifting of the bands. Ev is the top of the valence band and Ec and the bottom of the conduction band
(Figure 1.)

## Slide 42
(δίοδος=bergpas)
pn-overgang met extern spanningsverschil
voor zowel e- als gaten stelt zich een evenwicht in tussen drift- en diffusiestromen
sperstroom/donkerstroom
V in doorlaatrichting
 verarmingsgebied kleiner
V > drempelspanning:
verarmingsgebied verdwijnt
doorlaat
sper
http://www.pveducation.org/pvcdrom/diode-equation
https://en.wikibooks.org/wiki/Introduction_to_Inorganic_Chemistry/Electronic_Properties_of_Materials:_Superconductors_and_Semiconductors#_10.6_Diodes,_LEDs_and_solar_cells
Notes: https://fisluisabraham.files.wordpress.com/2014/08/krane-k-modern-physics-3ed.pdf
Drempelspanning: de doorlaatspanning bandgap silicium 0,01 eV en bandgap germanium 0,05 eV
Drempelspanning: de doorlaatspanning bandgap silicium 1,14 eV en bandgap germanium 0,67 eV
Voor een siliciumdiode ongeveer 0,6 volt, voor een germaniumdiode circa 0,25 volt. Licht emitterende diodes (leds) hebben hogere doorlaatspanningen, meestal tussen 2 en 4,6 volt. Schottkydioden hebben, door meer doping van het halfgeleidermateriaal, een lagere doorlaatspanning van ongeveer 0,2 volt.

## Slide 43
(δίοδος=bergpas)
Drift- en diffusiestroom
voor zowel e- als gaten stelt zich een evenwicht in tussen drift- en diffusiestromen
http://www.pveducation.org/pvcdrom/diode-equation
driftstroom: thermische energie  e- -gatpaar
ingebouwd E-veld trekt e- en gat uit elkaar
 driftstroom  als T 
diffusiestroom:  overmaat: n-type: e-
p-type: gaten
Er is een kans dat enkele
meerderheidsladingsdragers
genoeg snelheid hebben om, tegen het E-veld in,
het verarmingsgebied over te steken
 diffusiestroom  als T  (want <v>  en # e-mobiel  door Ethermisch)
 diffusiestroom  als Vext  (dit geldt extra sterk als Vext > Vdrempel )
donkerstroom (= diffusiestroom - driftstroom )  als T 
 driftstroom stijgt kennelijk harder
Notes: verschil metaal - intrinsieke halfgeleider - gedoteerde halfgeleider - #-5 materiaal?
aansluiten diode: gaten worden aangetrokken/elektronen worden aangetrokken, van depletiezone weg.
'glijbaandiagram' e- wegtrekken, gaten wegtrekken...
doorlaat:
e- injecteren, gaten injecteren...
meerderheids/ minderheidsladingsdragers:
onderscheid ruimte E-diagram
More recombination takes place. So we have more immobile ions at junction. Smaller gap is formed with higher density.
For silicon solar cells near room temperature, the Dark Saturation Current I0 approximately doubles for every 10 °C increase in temperature.
http://www.pveducation.org/pvcdrom/effect-of-temperature
https://www.youtube.com/watch?v=hIY4UaPkl38

## Slide 44
Netto stroom door diode (pn-overgang)
Zonder extern voltage: evenwicht tussen drift- en diffusiestroom van e-
# e- met E > Ec evenredig met f(E)
Externe spanning DVext  niveau naar E + e DVext
Netto stroom: verschil drift- en diffusiestroom:
diffusie of drift?
diffusiestroom
drift hangt alleen af van T
Notes: Bij kamertemperatuur is 1 verwaarloosbaar t.a.v. e^(E – E_F / kT)
https://fisluisabraham.files.wordpress.com/2014/08/krane-k-modern-physics-3ed.pdf

## Slide 45
I-V-karakteristiek diode

## Slide 46
Bij deze aansluiting zal een stroom gaan lopen.
De depletiezone is symmetrisch rondom de overgang
Stelling I en II beide fout
Stelling I en II beide goed
Stelling I fout en II goed
Stelling I goed en II fout
Quiz pn-overgang, zwaarder n-gedoteerd (N+)
Notes: Asymmetric doping of the p-n junction: The space charge region extends mainly into the low doping region http://www.textbook-pv.org/figures.html 16

## Slide 47
Bij deze aansluiting zal een stroom gaan lopen.
De depletiezone is symmetrisch rondom de overgang
Stelling I en II beide fout
Stelling I en II beide goed
Stelling I fout en II goed
Stelling I goed en II fout
Quiz pn-overgang
V < 0 p-kant: gaten worden aangetrokken, n-kant: e- worden weggetrokken
+
-
Notes: Asymmetric doping of the p-n junction: The space charge region extends mainly into the low doping region http://www.textbook-pv.org/figures.html 16

## Slide 48
+
(SCR) ook wel: depletiezone
Bij deze aansluiting zal een stroom gaan lopen.
De depletiezone is symmetrisch rondom de overgang
Stelling I en II beide fout
Stelling I en II beide goed
Stelling I fout en II goed
Stelling I goed en II fout
n+  pn-overgang zwaarder n-gedoteerd
https://en.wikipedia.org/wiki/Depletion_region#/media/File:Pn-junction-equilibrium-graphs.png
https://en.wikipedia.org/wiki/Depletion_region#Determining_the_depletion_layer_width
Notes: Asymmetric doping of the p-n junction: The space charge region extends mainly into the low doping region http://www.textbook-pv.org/figures.html 16

## Slide 49
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
http://micro.magnet.fsu.edu/primer/java/solarcell/
http://www.hk-phy.org/energy/alternate/solar_phy03_e.html
+
-
+
-
+
-
e- -gatpaar
gescheiden
alleen depletielaag actief
n-laag boven
Notes: Bohrdotering (p boven) geeft meteen beteren n voor AR-coating
Alleen depletielaag si actief, levert energie
als licht van boven invalt op pn  inefficiënt
daarom n-laag boven ipv rechts
Halfgeleider uit groep IV (Silicium, Germanium
Groep III: Boor, Gallium, Indium, Aluminium
Groep V: Fosfor; Arseen; Stikstof, Antimoon, Bismuth
http://www.hk-phy.org/energy/alternate/solar_phy03_e.html
http://www.see.murdoch.edu.au/resources/info/Tech/pv/
http://www.tf.uni-kiel.de/matwis/amat/semi_en/kap_2/backbone/r2_3_5.html
http://peterdoggart.com/wp-content/uploads/2012/10/Diode-Characteristics.pdf
When on the order of one dopant atom is added per 100 million atoms, the doping is said to be low or light. When many more dopant atoms are added, on the order of one per ten thousand atoms, the doping is referred to as heavy or high. This is often shown as n+ for n-type doping or p+ for p-type doping. (sensitors heavy; NTC and PTC light)

## Slide 50
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
Sperstroom van n naar p
P = V .I
lichtopval
 negatief vermogen
 stroombron
http://www.eternalsun.com/test-service-voor-zonnepanelen/
Maximum power point: ideale I en V
Notes: http://www.eternalsun.com/test-service-voor-zonnepanelen/
Principle of light absorption in the semiconductor. The photon is absorbed only with sufficient light energy and an electron is raised into the conduction band

## Slide 51
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
T   meer e--gat-paren
 driftstroom 
 ruimtelading 
 efficiëntie 
Wat is het effect van T?
Notes: http://www.zonnepanelen-info.nl/zonnepanelen/rendement-zonnepanelen/
de totale opbrengst van een zonnecel daalt met toename van de weerstand van de stroomkring.

## Slide 52
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
open-klemspanning (VOC)
pn-overgang goed: VOC (open-klemspanning) en kortsluitstroom (Isc) hoog
VOC max 1,2 V
Isc max 30 mA
kortsluitstroom (Isc):
elk geabsorbeerd foton
geeft bijdrage aan stroom
LED
Notes: The open-circuit voltage Voc is determined by the separation of the quasi Fermi levels in the n-doped and p-doped regions.

## Slide 53
Diode-laser
geïnverteerde populatie
grote kans op gestimuleerde emissie
(spiegels aan weerszijden nodig)
elektrisch
pompen
Notes: https://fisluisabraham.files.wordpress.com/2014/08/krane-k-modern-physics-3ed.pdf

## Slide 54
Diode-laser
spiegels:
cleaved
(splijten van de wafer)
(dicing)
buiging
vanwege
smalle
depletielaag
Notes: https://fisluisabraham.files.wordpress.com/2014/08/krane-k-modern-physics-3ed.pdf

## Slide 55
p-i-overgang
Wat gebeurt er nu?
intrinsic Si
NB: toevallige onzuiverheden in het intrinsiek Si gaan
nu een grote rol spelen!
Notes: https://www.intechopen.com/books/photodiodes-world-activities-in-2011/cmos-photodetectors
P-i-N photodiode
Increasing the active region where the signal generating photogenerated carriers originated from should in principle increase the collection efficiency. Previously, increasing the active region by increasing W through reverse biased was discussed. To further increase the active region, the device geometry can be altered to include an intrinsic region between the p-type and n-type regions, as shown in Figure 6, this results is a p-i-n junction.
Figure 6(e), shows a band diagram of a p-i-n junction under reverse bias. Under reverse bias, certain assumptions can be made because the external field has driven almost all the carriers from the intrinsic region [47]. These assumptions are,
No net charge in the intrinsic region.
A very narrow depletion region on the doped side of each of the doped-intrinsic junctions.
With these assumptions, the depletion layer width is simply the width of the intrinsic region; the electric field in the intrinsic region is simply,
E=qV 0 −VW , E=qV0-VW,
(14)OptionsView Equation
Bookmark
and the junction capacitance is given by Equation 11.
Consequently, the p-i-n photodiode under reverse bias can have a CPD smaller than a p-n junction photodiode, but the wider depletion region also implies a longer transit time. Therefore, transit time becomes the dominant limiting factor in the speed the device, and operating the device under sufficient reverse bias is essential, and quick estimation in [41] shows that the transit time of a carrier to cross the intrinsic layer is on the order 0.1 ns. Moreover, to optimize for quantum efficiency without sacrificing speed, it is common practice to design the intrinsic layer thickness to be larger than absorption length given by -1, but not much more [41]. Further discussion on p-i-n photodiodes can be found in references [40, 41].
Figure 6.
a) Structure, (b) carrier distribution, (c) charge distribution, (d) electric field, and (e) band diagram of P-I-N junction under reverse bias.

## Slide 56
PiN-fotodiode
https://www.slideshare.net/kalyanacharjya/photodetector-photodiode
depletion region is much larger than in a PN diode, and almost constant-size, independent of the reverse bias applied to the diode. This increases the volume where electron-hole pairs can be generated by an incident photon.
Notes: https://www.electronics-tutorials.ws/diode/diode_2.html
A p-i-n junction can be biased at a larger reverse bias before breakdown occurs (when the peak electric field exceeds a critical value, because the maximum electric field in a p-i-n junction is much lower than the peak electric field (>105 V/cm) in a pn junction (ref. Problem 1,2). www-inst.eecs.berkeley.edu/~ee130/sp13/homework/hw5soln.doc

## Slide 57
PiN-fotodiode
Na
Nd
Nd
Na
Notes: https://www.intechopen.com/books/photodiodes-world-activities-in-2011/cmos-photodetectors
https://www.intechopen.com/chapters/17220
P-i-N photodiode
Increasing the active region where the signal generating photogenerated carriers originated from should in principle increase the collection efficiency. Previously, increasing the active region by increasing W through reverse biased was discussed. To further increase the active region, the device geometry can be altered to include an intrinsic region between the p-type and n-type regions, as shown in Figure 6, this results is a p-i-n junction.
Figure 6(e), shows a band diagram of a p-i-n junction under reverse bias. Under reverse bias, certain assumptions can be made because the external field has driven almost all the carriers from the intrinsic region [47]. These assumptions are,
No net charge in the intrinsic region.
A very narrow depletion region on the doped side of each of the doped-intrinsic junctions.
With these assumptions, the depletion layer width is simply the width of the intrinsic region; the electric field in the intrinsic region is simply,
E=qV 0 −VW , E=qV0-VW,
(14)OptionsView Equation
Bookmark
and the junction capacitance is given by Equation 11.
Consequently, the p-i-n photodiode under reverse bias can have a CPD smaller than a p-n junction photodiode, but the wider depletion region also implies a longer transit time. Therefore, transit time becomes the dominant limiting factor in the speed the device, and operating the device under sufficient reverse bias is essential, and quick estimation in [41] shows that the transit time of a carrier to cross the intrinsic layer is on the order 0.1 ns. Moreover, to optimize for quantum efficiency without sacrificing speed, it is common practice to design the intrinsic layer thickness to be larger than absorption length given by -1, but not much more [41]. Further discussion on p-i-n photodiodes can be found in references [40, 41].
Figure 6.
a) Structure, (b) carrier distribution, (c) charge distribution, (d) electric field, and (e) band diagram of P-I-N junction under reverse bias.

## Slide 58
Intrinsieke halfgeleider (zuiver)   III-V-rooster
geleiding door:
e- in geleidingsband
gaten in valentieband
Notes: http://www.textbook-pv.org/figures.html

## Slide 59
III-V-rooster (intrinsiek)   II-VI-rooster (intrinsiek)
geleiding door:
e- in geleidingsband
gaten in valentieband
Notes: http://www.textbook-pv.org/figures.html

## Slide 60
Doorlezen: Giancoli t/m §40.10 + 11.3 & 11.7 uit Modern Physics
Maak Problems: 4045, 47, 74,75
en
Extra HW Opdrachten 3 t/m 5
Huiswerk

## Slide 61
p-n overgang (Vextern = 0)
Notes: https://www.electronics-tutorials.ws/diode/diode_2.html
A p-i-n junction can be biased at a larger reverse bias before breakdown occurs (when the peak electric field exceeds a critical value, because the maximum electric field in a p-i-n junction is much lower than the peak electric field (>105 V/cm) in a pn junction (ref. Problem 1,2). www-inst.eecs.berkeley.edu/~ee130/sp13/homework/hw5soln.doc

## Slide 62
Diode in doorlaatrichting ( V > Vdrempel )
https://en.wikibooks.org/wiki/Introduction_to_Inorganic_Chemistry/Electronic_Properties_of_Materials:_Superconductors_and_Semiconductors#_10.6_Diodes,_LEDs_and_solar_cells

## Slide 63
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
Equivalent circuit: constante stroombron levert IL
door omzetting van zonlicht naar elektrische stroom.
Notes: The open-circuit voltage Voc is determined by the separation of the quasi Fermi levels in the n-doped and p-doped regions.

## Slide 64
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
Notes: The open-circuit voltage Voc is determined by the separation of the quasi Fermi levels in the n-doped and p-doped regions.

## Slide 65
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
Notes: The open-circuit voltage Voc is determined by the separation of the quasi Fermi levels in the n-doped and p-doped regions.

## Slide 66
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
Notes: The open-circuit voltage Voc is determined by the separation of the quasi Fermi levels in the n-doped and p-doped regions.

## Slide 67
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
VOC (open-klemspanning) en kortsluitstroom (Isc) hoog,
maar te lage Rsh en te hoge Rs  lage efficiëntie
record: 28.8%
Shockley–Queisserlimiet: 33.7%
(één p-n junction
met band gap 1.34 eV)
Notes: The open-circuit voltage Voc is determined by the separation of the quasi Fermi levels in the n-doped and p-doped regions.

## Slide 68
Fotovoltaïsche cel (PV-cel: bekendste type zonnecel)
Notes: The open-circuit voltage Voc is determined by the separation of the quasi Fermi levels in the n-doped and p-doped regions.

## Slide 69
Avalanche-fotodiode (+ Zenerdiode voor U > 5,6V)
Notes: http://www.differencebetween.net/science/physics-science/difference-between-avalanche-breakdown-and-zener-breakdown/
At above 5 V, a Zener diode has a positive temperature coefficient, which means that Zener voltage increases with temperature. (avalanche breakdown):
At below 5 V, it shows a negative temperature coefficient; Zener voltage decreases as temperature rises. (Zener breakdown):
as the temperature increases the thermal vibration increases and the mean free path decreases. In this free path the primary electrons or holes get accelerated strongly enough to knock out electrons from the valence band to the conduction band. Since the path length gets smaller, then the electrons or holes will need larger electric field to acquire kinetic energy equal or greater then the energy gap. To increase the electric field one has to increase the voltage. Hence, the breakdown voltage increases with the temperature increase.

## Slide 70
Avalanche-fotodiode
Notes: https://www.intechopen.com/books/photodiodes-world-activities-in-2011/cmos-photodetectors
Avalanche photodiode
The avalanche photodiode (APD) is the solid state equivalent of a photomultiplier tube. Its main application is for detection of weak optical signal such as single photon events. The APD exploits the impact ionization of carriers by photogenerated carriers under extremely high reverse bias. During its operation, carriers that trigger impact ionization and the carriers that are generated by impact ionization continue to drift to cause more impact ionization events to occur. The result is a cascade of impact ionization events that produces an avalanche effect to amplify the photogenerated current. The amplification of the current is given by a multiplication factor, M = Imph / Iph. It is fundamentally related to the ionization coefficients of the carrier by the follow Equation,
1−1M =∪ 0 W Ϗ n exp[−∪ x W (Ϗ n −Ϗ p )dx']dx 1-1M=∪0WϏnexp-∪xWϏn-Ϗpdx'dx
(15)OptionsView Equation
Bookmark
where,n and p are the ionization coefficients of the electrons and holes respectively [48]. Empirically, it can be approximated by,
M=11−(VV BD ) n M=11-VVBDn
(16)OptionsView Equation
Bookmark
where, n is material dependent parameter [49]. When taking the dark current into account, it becomes
M=11−(V−IR'V BD ) n M=11-V-IR'VBDn
(17)OptionsView Equation
Bookmark
where,I is the total current following through the APD, and R’ is the differential resistance observed in junction breakdown [50]. Because the random nature of impact ionization, APD suffers from another form of statistical noise call excessive noise [41]. It is given by,
F=M[1−(1−k)(M−1M ) 2 ] F=M1-1-kM-1M2
(18)OptionsView Equation
Bookmark
where, k is the ratio n/p.
An APD can also be operated in Geiger mode under reverse bias beyond the breakdown voltage. In this case, an electron-hole pair generated by a single photon will trigger the avalanche effect that generates a large current signal. Therefore, photon counting (like particle counting with a Geiger counter) can be achieved in Geiger mode. An APD that can operate in Geiger mode is also known as a single photon avalanche diode (SPAD).
Figure 7.
The cross-section of a SPAD CMOS sensor [51] showing the guard ring surrounding the active region.
Because APDs operate in or near the breakdown region, a physical feature known as a guard ring around the active region is used prevent surface breakdown, as shown in Figure 7. Moreover, the high reverse bias voltage required to produce the avalanche effect had hindered the incorporation of CMOS technology with APD. In 2000, Biber et al. at Centre Suisse d’Electronique et de Microtechnique (CSEM) produced a 1224 pixel APD fabricated in standard BiCMOS technology [52, 53]. Since that pioneering work, there has been a steady growth in the development of CMOS APD [54-56] and CMOS SPAD [51, 57-61] for application such as fluorescence sensing [51, 62, 63] and particle detection [64].

## Slide 71
Zenerdiode voor U < 5,6V : tunneling
Zenerdiode:
voorspelbaar + herbruikbaar
extra hoge dotering
extra lage toleranties

## Slide 72
Fermi-energie: T = 0K Fermi-niveau: elke T.
energy difference total energy level (kinetic and potential energy)
statische potentiaalput/-banden ook bij niet-evenwicht-situaties
The Fermi level is the total chemical potential for electrons (or electrochemical potential for electrons) and is usually denoted by µ or EF.[1] The Fermi level of a body is a thermodynamic quantity, and its significance is the thermodynamic work required to add one electron to the body (not counting the work required to remove the electron from wherever it came from).
Fermi-energie   Ferminiveau
Notes: Figure 40-36. Impurity energy levels in doped semiconductors.